## Slide 1: Parts Options
Group 1

## Slide 2
Extras:
4 LEDs
2 Buttons
Extras:
1 LED
1 Buttons
Previous Selection: Arduino Uno

## Slide 4: GPS Module (Adafruit Ultimate GPS Module)
Sensitivity
  ~ 3 meters
Power Consumption
  Voltage
    3-5.5V
  Current
    20 mA during navigation
Dimensions
  Breakout: 1.0" x 1.35" x 0.25"
  IC: 0.63” x 0.63”
Cost
  $30-40

## Slide 5: Software for Telemetry

## Slide 6: Software for GPS

## Slide 7: Antenna - U. Fl

## Slide 8: Buzzer Options
PUI Audio Inc. AI-1223-TWT-3V-2-R
2-4VDC Operating
30mA max
Through Hole PCB mount
12mm diameter, 8mm height
82 dBA @ 10cm
$1.33 on DigiKey
PUI Audio Inc. X-4033-TF-LW80-R
Highest dBA below @ voltage below 12 VDC
1.5-12 VDC Operating
9mA max
Wire Leads, panel mount flange
50mm diameter, 23mm height
106 dBA @ 10cm
$7.43 on DigiKey

## Slide 9: Vibrator Options
Cylinder with Half-Moon Rotator
Solder on, lead wire options
3VDC operation
Check Operating Voltage level (2.7~3.3)
4.5x4.85x10.9 mm
$2.70-$4.50
How to mount? Harness?
Coin Vibrator Motor
Solder tab, lead wire options
3 VDC operation
Check Operating Voltage level (2.7~3.3)
9mm diameter, 2.25mm height
$1.22-$4.50
How to mount? Glue?

## Slide 10: Battery
Using microcontroller ADC to measure battery charge
Battery options:
Lithium rechargeable battery
Store bought coin battery
Size will be based on power needed by other major components

## Slide 11: Concerns to bring up at sponsor meeting
Choose between battery life and physical size
Not going to meet dB constraint
Revisit using GPS with sponsor